## Slide 1
The Noisy Neighbour
Inside Your GPU
Observing Batched LLM Inference
Sagar Utekar · Senior SRE, CrowdStrike
CNCF Ambassador · Kubestronaut
Observability Summit Europe 2026
5 Oct · 10:30 · South Hall 3A
Notes: Hi, I'm Sagar. I run GPU infrastructure for AI workloads at CrowdStrike. Today we're hunting a ghost — a latency spike you can see on your dashboard but can't explain with your traces. The victim is Alex. The culprit is Blake. And they both live inside the same GPU.

## Slide 2
The Neighbour You Already Know
🔥 The CPU Problem
Container B is a rogue batch job
Steals CPU from your app
Latency spikes. No errors.
container_cpu_cfs_throttled_seconds_total
✅ How You Fixed It
cgroups → kernel isolation
Resource limits → cap the bully
Node pools → physical separation
Anti-affinity → scheduling rules
CPU noisy neighbours? Solved. You had soundproof walls.
Notes: You've all debugged this. Container B eats CPU, your app gets throttled. You fixed it with cgroups — soundproof walls between tenants. Resource limits, node pools, anti-affinity. Problem solved. [PAUSE] Now let's talk about a building with no soundproofing.

## Slide 3
Now Forget Everything
CPU World 🏢
✓ cgroups
✓ Resource limits
✓ 1 process = 1 core
✓ Isolation is cheap
GPU World 🏚️
✗ No cgroups
✗ No per-request limits
✗ 32 requests = 1 chip
✗ Isolation kills throughput
On a GPU, requests MUST share the chip. The walls are paper-thin.
The fix isn't soundproofing — it's installing noise monitors.
Notes: [PAUSE — let the table sink in] GPUs don't have cgroups. There are no soundproof walls. 32 requests share one chip at the same time. You could isolate — run one request per GPU — but you'd use 10% of a $40,000 card. The fix isn't isolation. It's observability. That's what this talk is about.

## Slide 4
The Apartment Building
🏢 GPU = The Building (the whole chip)
🛗 Batch = The Elevator (shared — one trip serves everyone)
🧳 KV Cache = The Storage Room (everyone's stuff piles up)
👤 Requests = Tenants (some quick, some... not)
📦 Preemption = Eviction (your stuff moved to the basement)
Keep this picture. Every slide from here maps back to it.
Notes: This is the mental model for the whole talk. GPU is an apartment building. The batch is the elevator — everyone shares it. KV cache is the storage room — every tenant's stuff accumulates. When the storage room fills, someone gets evicted. Keep this picture — everything maps back to it.

## Slide 5
Two Phases, Two Numbers
PREFILL
Read the request. Once.
Compute-bound — GPU loves this
DECODE
Write back, one token at a time.
Memory-bound — GPU waits
TTFT
Time to First Token
= elevator wait time
ITL
Inter-Token Latency
= elevator speed ← THE SIGNAL
Notes: Every LLM reply has two phases. Prefill reads your request — fast, once. Decode writes back one token at a time — slow, hundreds of times. Two numbers to know: TTFT is how long before the first word appears — that's the elevator wait. ITL is the gap between each word — that's how fast the elevator moves. [PAUSE] ITL is THE noisy neighbour signal. When Blake loads furniture in the elevator, ITL is what spikes.

## Slide 6
Meet Your Neighbours
ALEX
The Quiet Tenant
💬 'Summarise this Jira ticket'
📏 64 tokens — a quick note
⚡ In and out in minutes
Alex will file the noise complaint.
BLAKE
The Renovator
📊 'Write a capacity report'
📏 4,000 tokens — a 5-page plan
🔨 Same building, same elevator
Blake is about to ruin Alex's morning.
Notes: Meet your neighbours. Alex sends a quick question — 64 tokens, like a note under the door. Blake wants a 5-page capacity report — 4,000 tokens. They're in the same building, sharing the same elevator, sharing every single trip. Alex is about to have a bad morning.

## Slide 7
Why Everyone Shares the Elevator
1 tenant
10%
GPU utilization
You pay for 100% of the building.
8 tenants
65%
GPU utilization
Same building, 8× the revenue.
Continuous batching: check after every trip. Slot opens → fill it.
36× more tenants served vs. static batching (Orca, 2022)
But now everyone shares the elevator. Blake's furniture slows it for everyone.
Notes: One tenant on a GPU — 10% utilized. You're paying for a building that's 90% empty. Batch 8 tenants — 65% utilized. Continuous batching checks after every elevator trip: someone got off? Fill the spot immediately. 36× more tenants served. [PAUSE] But now they all share every trip. Blake's renovation materials slow the elevator for everyone.

## Slide 8
The Storage Room Crisis
KV Cache — every token adds to the pile
Alex
Alex
Alex
8%
of room
Blake
Blake
Blake
Blake
Blake
Blake
79%
of room
Blake's 4,000 tokens = ~4 GB of GPU memory
⚠️ STORAGE FULL → EVICTION
Alex's stuff moved to basement. Must re-register when rescheduled.
That's your mystery TTFT spike.
vllm:kv_cache_usage_perc >85% = danger zone
Notes: KV cache is the storage room. Every token generated adds to the pile. Alex's 64 tokens — three small boxes, 8% of the room. Blake's 4,000 tokens — fills 79% of the room, about 4 gigabytes. When storage hits capacity, someone gets evicted. Their stuff goes to the basement — CPU memory or disk. When they get rescheduled, they must re-prefill from scratch. That's your mystery TTFT spike — it's not a new request, it's a re-registering tenant.

## Slide 9
What Alex Experiences
🟢 Alex alone:
TTFT 82ms → ITL 14ms × 64 tokens → Done in 210ms
Express elevator. Smooth.
🔴 Alex + Blake in batch:
TTFT 120ms → ITL 45ms × 64 tokens → Done in 482ms
Same 64 tokens. 2.3× slower. Zero errors.
ITL × tokens = phantom latency
The elevator slowed. Alex didn't change. The building did.
Notes: Here's what Alex feels. Alone: elevator wait 82ms, each floor 14ms, done in 210ms. With Blake: elevator wait 120ms, each floor 45ms — same 64 tokens, 2.3× slower, zero errors, zero timeouts. [PAUSE] ITL times tokens equals phantom latency. The elevator slowed down. Alex didn't change. The building did.

## Slide 10
Your Dashboard Lies
What RED Shows
RATE ✓
ERRORS 0
P99 1.8s ✗
Conclusion: slow tenants. Build more buildings.
What Actually Happened
190ms
1,610ms WAITING
• Storage: 94% full
• Occupancy: 28 tenants
• Blake: generating 3,000+ tokens
• Alex: evicted twice
The tenant was fine. The building was noisy.
Notes: Your RED dashboard says: rate fine, errors zero, p99 is 1.8 seconds. Conclusion: slow tenants, build more buildings. [PAUSE] Wrong. That 1,800ms was 190 milliseconds of actual compute and 1,610 milliseconds of waiting. KV cache 94% full. 28 tenants in the batch. Blake generating 3,000 tokens. Alex got evicted twice. The tenant was fine. The building was noisy.

## Slide 11
Three Causes of Latency
🕐
SCHEDULING
Waiting in the lobby
vllm:num_requests_waiting
Fix: Build more buildings
🧠
MEMORY
Storage full → evictions
vllm:kv_cache_usage_perc
Fix: Occupancy cap + shared storage
👥
NEIGHBOUR
Elevator slowed by renovators
vllm:inter_token_latency_seconds
Fix: Renovators → different building
Your dashboard shows the complaint. These three tell you the cause.
Notes: Three causes. Scheduling — people waiting in the lobby, real capacity limit, build more buildings. Memory — storage room full, evictions, cap the occupancy and enable shared storage. Neighbour — Blake's furniture in the elevator, route renovators to a different building. Your dashboard shows the complaint. These three tell you the actual cause.

## Slide 12
The Monitoring System
GRAFANA
Security cameras
↓ queries
PROMETHEUS
Sensor network (every 15s)
↙
↘
vLLM /metrics
Elevator, storage, lobby
DCGM Exporter
Power, temperature, structure
Four components. All open-source. No vendor lock-in.
Notes: Quick architecture slide. Grafana is the security camera. Prometheus is the sensor network scraping every 15 seconds. Two sources: vLLM metrics for elevator speed, storage, lobby — that's the application layer. DCGM Exporter for power, temperature, structural load — that's the GPU hardware layer. Four components, all open-source. Moving on.

## Slide 13
[PRE-RECORDED] Quiet Sunday Morning
5 Alexes. All quiet. Replace with Grafana screenshot.
TTFT p99
82ms
ITL p99
14ms
Storage
18%
Occupancy
5
Power
38%
Lobby
0
Everything flat. Everything green. Remember these numbers.
Notes: This is the pre-recorded baseline. Five Alexes, quiet Sunday morning. [Read each metric] TTFT 82 milliseconds. ITL 14 milliseconds. Storage 18%. Occupancy 5. Power 38%. Lobby zero. [PAUSE] Everything flat. Everything green. Remember these six numbers. I'm about to change three of them dramatically.

## Slide 14
[DEMO] The Renovators Arrive
+3 Blakes. Same building. Alex didn't change — the building did.
TTFT
82 → 420ms
▲ 5×
ITL
14 → 43ms
▲ 3×
Storage
18 → 87%
▲ DANGER
Occupancy
5 → 8
▲ +3
Power
38 → 74%
▲ 2×
Lobby
0
✓ STILL ZERO
Lobby is EMPTY. It's not a building shortage. It's a neighbour problem.
Notes: [Dramatic pause before revealing each metric] Three Blakes move in. TTFT — 5× slower. ITL — 3× slower. Storage jumps to 87 percent. Occupancy goes to 8. Power doubles to 74. [LONG PAUSE] And the lobby? Still zero. Nobody is waiting to get in. [PAUSE] This is not a building shortage. This is a noisy neighbour problem. The GPU isn't overloaded — it's sharing badly.

## Slide 15
The Chain Reaction
Blake moves in
→
Occupancy 5→8
→
Storage 18→87%
→
Evictions start
→
ITL 14→43ms
→
Alex: 210→482ms
More renovators × more stuff = slower elevator for everyone
❌ Dashboard: GPU 74%, p99 up → BUILD MORE BUILDINGS
✓ Reality: Cap occupancy. Rehouse renovators. → FEWER NEIGHBOURS
Notes: The chain reaction in one picture. Blake moves in. Occupancy grows. Storage fills. Evictions start. ITL spikes. Alex goes from 210 to 482 milliseconds. [PAUSE] Your dashboard says: GPU at 74%, latency doubled, build more buildings. The real answer: cap the occupancy, send renovators to their own building. You don't need more buildings. You need fewer neighbours.

## Slide 16
Six Sensors for Your Building
📸 Take a photo of this slide.
🔵 Elevator Wait (TTFT p99)
histogram_quantile(0.99, rate(vllm:time_to_first_token_seconds_bucket[5m]))
How long to get in?
🟡 Elevator Speed (ITL p99) — THE SIGNAL
histogram_quantile(0.99, rate(vllm:inter_token_latency_seconds_bucket[5m]))
How fast does it move?
🟠 Storage (KV Cache)
vllm:kv_cache_usage_perc
>85% = danger zone
🟣 Shared Storage Hits
rate(vllm:prefix_cache_hits[5m]) / rate(vllm:prefix_cache_queries[5m])
Re-reading the same mail?
🟣 Occupancy (Batch)
vllm:num_requests_running
How crowded is the building?
🔴 Power Load (Tensor)
DCGM_FI_PROF_PIPE_TENSOR_ACTIVE
Computing or idling?
Notes: Six sensors. Take a photo — this is what you'll build Monday. [Point to each] TTFT: elevator wait. ITL — THE signal — elevator speed. KV cache: storage fullness, over 85% is danger. Prefix cache hit rate: are we re-reading mail we already read? Batch size: building occupancy. Tensor core: is the GPU actually working or just heating the room? ITL is number two and it's the one that changes everything.

## Slide 17
Three Alarms. Not Thirty.
⚠️ Storage > 90% for 2 minutes
Evictions imminent. Cap occupancy immediately.
🚨 Elevator wait > 2s for 5 minutes
Tenants banging on doors. Scale or shed load.
📊 Lobby > 0 for 3 minutes
Real building shortage. Build more.
Three alarms. Not thirty.
Notes: Three alarms. Storage over 90% for 2 minutes — evictions are imminent, cap occupancy now. TTFT over 2 seconds for 5 minutes — tenants are banging on the door, scale up or shed load. Lobby greater than zero for 3 minutes — this is a real capacity limit, time to build more. Three alarms. Not thirty. You can set these up in 20 minutes.

## Slide 18
Taming the Renovators
1. Occupancy Cap
--max-num-seqs 16
Default is 256. Start at 16.
Watch ITL as you tune up.
2. Separate Building
Route by estimated output length
Short requests (<256 tok) → Pool A
Long requests (>256 tok) → Pool B
3. Shared Storage
--enable-prefix-caching
Same system prompt → share the cache
30-50% memory savings
4. Scale on Lobby
Lobby count = leading indicator
Power usage = lagging indicator
Scale when lobby > 0, not power > 80%
Notes: Four ways to tame Blake. [One] Cap occupancy at 16 — the default is 256, that's 256 tenants sharing one elevator, madness. Start at 16, watch ITL as you tune up. [Two] Separate building — route short and long requests to different GPU pools. [Three] Enable shared storage — prefix caching reuses KV cache for common system prompts, saves 30-50% memory. [Four] Scale on lobby count, not power usage. Lobby is a leading indicator. Power is lagging.

## Slide 19
PagedAttention: Why This Works
Before
Contiguous memory allocation
Pre-reserve max context per request
60-80% of allocated memory WASTED
Can't do continuous batching efficiently
After (vLLM)
Virtual memory-style paging
Fixed-size blocks allocated on demand
Near-zero waste
Enables dynamic slot-filling
🔗 Interactive visualization: understandingdata.com/ai-engineering-visualised/kv-cache/
Credit: James Phoenix
Notes: Why does continuous batching actually work? PagedAttention. Before: you pre-reserved the full context length for every request — like reserving an entire storage unit for each tenant even if they only bring one box. 60 to 80 percent waste. After: vLLM allocates fixed-size blocks on demand, like virtual memory. Near-zero waste. This is what enables dynamic slot-filling. James Phoenix has an amazing interactive visualization of this at understandingdata.com — link is on the slide.

## Slide 20
Advanced: Disaggregate Prefill & Decode
The Conflict
Prefill = compute-heavy (GPU goes brrrr)
Decode = memory-heavy (GPU waits)
Running both on same GPU → head-of-line blocking
Blake's prefill starves Alex's decode
The Fix
Prefill workers ← dedicated pool
Decode workers ← dedicated pool
TTFT stays fast (prefill not blocked)
ITL stays stable (decode not starved)
Emerging pattern in TensorRT-LLM, Sarathi-Serve, Splitwise. Watch this space.
Notes: For the advanced folks. The prefill phase is compute-bound — GPU loves it. The decode phase is memory-bound — GPU waits. Running both on the same device causes head-of-line blocking. Blake's massive prefill starves Alex's decode. The cutting-edge fix: separate worker pools. Prefill goes to dedicated GPUs. Decode goes to dedicated GPUs. TTFT stays fast. ITL stays stable. This is emerging in TensorRT-LLM and Sarathi-Serve. Watch this space.

## Slide 21
Monday Morning
□ Install elevator sensors → vLLM /metrics to Prometheus
□ Install power monitors → DCGM Exporter on GPU nodes
□ Build the 6-sensor dashboard (slide 16)
□ Set the 3 alarms (slide 17)
□ Set occupancy cap → --max-num-seqs 16, watch ITL
□ Enable shared storage → --enable-prefix-caching
2-4 hours to install. 50-70% fewer complaints on mixed-tenant buildings.
Notes: Monday morning, six items. Install elevator sensors — expose vLLM metrics to Prometheus. Install power monitors — DCGM Exporter on your GPU nodes. Build the six-sensor dashboard from slide 16. Set the three alarms from slide 17. Cap occupancy at 16, watch ITL as you tune. Enable shared storage with prefix caching. Two to four hours of work. 50 to 70 percent p99 reduction on mixed workloads. That's the ROI of observing your neighbours.

## Slide 22
Next time your LLM p99 spikes...
don't ask 'which tenant is slow?'
Ask: 'who else is in the building?'
Notes: [Slow, deliberate delivery] Next time your LLM p99 spikes... don't ask which tenant is slow. [PAUSE] Ask: who else is in the building. [PAUSE] Thank you.

## Slide 23
Resources
📊 Dashboard & Demo github.com/Sagar2366/gpu-noisy-neighbour
🎥 KV Cache Visual understandingdata.com/ai-engineering-visualised/kv-cache/
🎥 Prefill/Decode Visual understandingdata.com/ai-engineering-visualised/prefill-decode/
📄 PagedAttention Paper arxiv.org/abs/2309.06180
📄 Orca Paper arxiv.org/abs/2206.00364
📄 Continuous Batching Explainer pub.towardsai.net — Vedanti
🐦 @SaijUtekar
Animations credit: James Phoenix / understandingdata.com
Notes: Everything's on GitHub — the slides, the demo infrastructure, the Grafana dashboard, the load generator. The links to James Phoenix's visualizations are there too — amazing interactive explainers for KV cache and prefill/decode. Find me on Twitter at @SaijUtekar. Questions?

## Slide 24
Q & A
github.com/Sagar2366/gpu-noisy-neighbour
@SaijUtekar
Notes: Prepared answers — [1] TGI: yes, same dynamics, different metric names. [2] Multi-GPU / tensor parallelism: same problem, batch shared across all GPUs in the TP group. [3] How to route by length without knowing output in advance: estimate from prompt structure + historical data, 'write a detailed report' → long pool. [4] Can you just set max_num_seqs to 1: yes but throughput drops 10-20×, the goal is managing not disabling. [5] What model size matters: any model using continuous batching, more visible with larger models because KV per token is bigger.